# Rugged™ Zinc-Free AW Hydraulic Oil

Rugged™ Zinc-Free AW Hydraulic Oil is high quality zinc-free hydraulic oil offering excellent oxidation protection with a unique zinc-free anti-wear additive system. Rugged™ Zinc-Free AW oils is available in an ISO 46 viscosity range to meet many equipment specifications.

Rugged™ Zinc-Free AW Hydraulic Oil is formulated to replace conventional zinc-containing hydraulic fluids where the environment is of utmost concern.

These applications include equipment used in marine environments, parks, wild life areas, recreational areas, golf courses, etc.  Rugged™ Zinc-Free AW Hydraulic Oil minimizes the environmental impact of accidental leaks and spills.

Recommended Applications:

- Fives Cincinnati P-70 Approved

- U.S. Steel 127

- DIN 51524 Parts 2

- DIN 51506, VDL Performance also for lower grades

- Parker Hannifin (Denison) HF-0, HF-1, HF-2

- Eaton-Vickers I-286-S

- Eaton-Vickers M-2950-S

- Eaton-Vickers 35VQ24A

- German Steel Industry SEB 181222

- ISO 11158:1997, Family H (Hydraulic Systems), Type HM

- US EPA/US Coast Guard Static Sheen Test

Important Characteristics:

Rugged™ Zinc-Free AW Hydraulic Oil is blended with selected premium quality base oils and selected additives to provide these essential characteristics:

- Biodegradable (OECD-301B).

- Contains no Zinc or other heavy metals.

- Extended oil life and pump durability.

- Antiwear and EP performance.

- Filteribility and demulsibility.

- Excellent thermal and oxidation stability.

# Rugged™ Zinc-Free AW Hydraulic Oil

| TYPICAL PROPERTIES |
| --- |
| ISO-Viscosity Grade | ASTM D-2422 | 46 |
| Specific Gravity | ASTM D-4052 | .865 |
| Flash Point F | ASTM D-92 | 464 |
| Pour Point F | ASTM D-97 | -33 |
| Viscosity @ 40 C | ASTM D-445 | 46 |
| Viscosity @ 100 C | ASTM D-445 | 6.9 |
| Viscosity Index | ASTM D-2270 | 105 |
| ASTM Rust Test | ASTM D-665 A&B | Pass |
| Oxidation Test | ASTM D-943 | 8000 |
| Foam, 3-sequences | ASTM D-892 | Pass |
| Acid Number mg KOH/g | ASTM D974 | 0.22 |
| Copper Corrosion | ASTM D130 | 1a |
| Demulsibility Minutes to pass | ASTM D1401 | 10 |
| Dielectric Strength (at manufacture) kV | ASTM D877 | 35 |
| Foam Test Seq I, mL | ASTM D892 | 0/0 |
| FZG Scuffing Test – failure load stage | ASTM D5182 | >12 |
| Oxidation Stability- TOST- hours | ASTM D943 | 8000 |
| Aquatic Toxicity, Rainbow Trout 1000mg/L 96h LC50 | OECD 203 1-12 | Non-toxic |
| Biodegradability in 28 days | OECD 301B, % | 20-59 |

A superior product by Colorado Petroleum Products Company

08-16-2017 JDS